| PROJECT NAME： GSe Pro 1000 series | Rev.：1.0 |
| --- | --- |
| DESCRIPTION: (ref): GSe Pro 1004 series 1U4-bay RAID subsystem, Generic controller, SATA2, Intel Avoton C2538 GSe Pro 1008 series 2U/8-bay RAID subsystem, Generic controller, SATA2, Intel Avoton C2538 |
| PRODUCT MANAGER：Glenn.Lee | DATE：2017/06/06 |
| MODEL NAME / NUMBER : Gse Pro 1000 serial models Gse Pro 1004 + no optional host boards Gse Pro 1008 + no optional host boards |
| APPROVED： FW PM HW TM FW TM ME TM SW TM |
| PROJECT ORIGINATOR | PM MANAGER |
| NOTIFY： |
| SALE | SOFTWARE | HARDWARE | MFG. MGR. | GEN.MGR. |  |  |
| Change History List |
| Rev | Update Reason | Updated Date | Updated By | Approved By |
| 1.0 | New Release | 2017/06/06 | Glenn.Lee |  |

Section 1: Overall view for whole product

| Category | Functional Specification | Remark |
| --- | --- | --- |
| Innovation | First IFT cloud gateway product |  |
| EonStor serial models products definition | Per C0 spec., EonStor GS serial models are: GSe Pro 1004 GSe Pro 1008 EonStor FS C0 MKT document: \\server02\Marketing\Product Planning\C0\Unify storage\Cloud Gateway HDD Bundle policy: Any number of "Drive + Plastic Tray" HDD types and q’ty are defined by Planning Cloud Gateway Product feature: Please follow the latest GS product feature: Host Board Support types: No host board design GSe Pro 1000 series Performance requirement: Product Family GSe Pro 1000 CPU Avoton C2538 Drive side interface SATA 6G GSe File read (MB/s) 400 GSe File write (MB/s) 400 GSe Pro 1000 series JBOD Support Models and Max Drive Policy: N/A |  |
| DIMM Configuration Requirements | Default configuration: 4GBx1 Support DDR3 up to 32G (16Gx2) Optional configurations: 8G (4G x2), 16G (8Gx2), 32G (16Gx2) |  |
| Super Cap and SSD requirements | No Super Cap. |  |
| Push button requirement | For Reset CTRL to Restore default Status |  |
| LCD and LED Requirements | Only support LED PNL; HW design reserve LCD LED follows ES_LED_FP_v1.22 or later version |  |
| HDD Support requirements | Support mixing SATA 3G/6G drives on AVL Support SATA-SSD (SSD: follow HDD AVL plan) |  |
| Form-factor requirements | Follow Enhance 3US and 2US ME design. |  |
| RoHS requirement | RoHS complaint is a MUST from development stage |  |
| PSU Requirements | For 2U12/3U16 platform: 3Y-460W RAID Form-factor Enclosure Name Controller PSU Vendor 1U4 1Ux Generic 250 Watt Delta 2U8 2Ux Generic 250 Watt Delta |  |
| Patent Concern | N.A. |  |
| MTBF | Controller: 500,000 hours Subsystem: 25,000 hours Power supplies: 250,000 hours Fans: 500,000 hours |  |
| EMC / Safety | Certification product names: should follow IFT business method of CTO EMC: BSMI, FCC / CE Class A (Class A is Acceptable). Safety: UL / cUL, CB, and ROSTEST (Russia Certificate) |  |
| Env. | Thermal: System working temperature should follow specs. Normal Operating: The temperature should be below 40C. Abnormal Operating (FANx1 or PSUx1 Failure): The temperature should remain below 40C Due to CPU spec, it cannot operate below 5C. Please test the system above 5C or equal to 5C to meet the CPU spec. Thermal concern Super Cap the Spec of Super cap is -25C~60C, Therefore it is recommend that w/o Super cap installed the room temperature cannot over 40C and W super cap installed the room temperature cannot over 40C. |  |
| Interoperability Req. | Refer to TD-4-06 Interoperability Test item of later version for SxF |  |

Section 2: User interface and customer related information

| Category | Functional Specification | Remark |
| --- | --- | --- |
| Connectors of rear-side of CTRL | For Single CTRL 1* mini USB connectors provide COM1 connectivity to HST. 4* RJ-45 connectors (1 in 1) provide 1GB (Management?) function – on Main board 2* USB 2.0 connector – on Main board 2* USB 3.0 connector – on Main board |  |
| CTRL Drawing |  |  |
| LED indicator on CTRL | Please refer to ES_LED_FP_v1.22 or later version for detailed LED definitions Ctrl 1 LED in green/Amber, for Controller Status Ctrl 2 LED in amber, for Cache Dirty status Steady on 1. Cache Memory is dirty or 2. Flushing data from FBM to drive (when power back) Blink Writing cached data from cache memory to FBM* during power outage. Once writing is done, all LEDs are turned off. Off No data is in cache memory Note : FBM : Flash Backup Module Ctrl 3 LEDs in green/amber to indicate CBM* Status Steady on in Green CBM is ready which means BBU (Super Cap.) and SSD Card both are present Blink in Green BBU (Super Cap.) is charging Steady on in Amber 1. BBU (Super Cap.) or SSD Card or both failed 2. No BBU (Super Cap.) and/or SSD Card are found in Redundant models. Off BBU (Super Cap.) is not installed in Generic Models Note : CBM: Cashe Backup Module Ctrl 4 LED in green, Fast Blink for Host Busy Restore Default Button: LED in GREEN, the default of NVRAM is restored Management Port *1 (1 in 1 connector): Speed LED on RJ-45 in green for 1G and blank for 10/100, Active LED Blink for LAN is active iSCSI 1G *4 ports (1 in 1 connector): Speed LED on 4x RJ-45 in green for 1G and blank for 10/100, Active LED Blink for LAN is active |  |

Section 3：CTRL PCBA and Host Board PCBA requirement

| Category | Functional Specification | Remark |
| --- | --- | --- |
| 1U4/2U8: RAID engine G Models CTRL PCBA (3822GSP04E and 3822GSP08E) | For GSe Pro 1004 Models CTRL : For 2U/3U serial RAID engines CTRL use the same PCBA (PCBA named as 3822GSP04E) For GSe Pro 1008 Models CTRL : For 2U/3U serial RAID engines CTRL use the same PCBA (PCBA named as 3822GSP08E) The design needs to keep the flexibility. |  |
| DRV backplanes | Different products use different Base-units w/ DRV BP PCBAs. And naming are listed as below: F/F G/R Base-unit DRV BP PCB DRV BP PCBA Models 1U4 G ESS04G2B2Dx-0035 9583ADP04G 9583ADP04G GSe Pro 1004 2U8 G ESS08G2B2Dx-0035 9583ADP08G 9583ADP08G GSe Pro 1008 Note 1. D means EonStor DS, x=0 means no bundle HDD and x=P means half qty of bundle HDD (8 for 3U, and 6 for 2U) Please refer to ESS16F-X1840_FTS_V1.0 or later version for detail spec Please refer to \\Server02\pm\PCC infor system\A667_models_naming for Enclosure/PCBA naming |  |
| 1U4: other small boards | Power board: 9583PWR1U 1U height, redundant PSU design. |  |
| 2U8: Other small boards | Power board: 9583PWR2U 2U height, redundant PSU design. Adaptor board: 9583ADP To access Power board and Backplane. |  |
| Cache Backup Module for Caching Data | R CTRLs are having Cache Backup Module for default. G CTRLs are option. |  |
| FW feature spec | Use FW v3.91 or later version (follow EonStor G6) |  |
| SW feature spec | Use SW v2.3.x or later version (follow EonStor G6) |  |

Appendix 1: CTRL Key parts and general information of each model

| Controller | DS RAID CTRL |
| --- | --- |
| 3822GSP04E | GSe Pro 1004 |
| 3822GSP08E | GSe Pro 1008 |
| Memory module per CTRL |  |
| DDRIII 4GB | Default, 4GB*1 |
| DDRIII 8GB | Optional, 4GB*2 |
| DDRIII 16GB | Optional, 8GB*2 |
| DDRIII 32GB | Optional, 16GB*2 |

Appendix 2: Spare parts and Accessories

| CTRL FRU P/N | GSe Pro 1004 | GSe Pro 1008 |
| --- | --- | --- |
| 3822GSP04E | V |  |
| 3822GSP08E |  | V |

| GSe Pro 1000 Series |
| --- |
| BP FRU P/N | GSe Pro 1004 | GSe Pro 1008 |
| 9583ADP04G | V |  |
| 9583ADP08G |  | V |
| Level-1 | Level-2 | FRU P/N | GSe Pro 1000 |
| Cables | Mini USB Cable | 9370ASCAB-0010 | Y |

### 2. Enclosure FRU

| Level-1 | FRU P/N | GSe Pro 1000 |
| --- | --- | --- |
| PSU | 9583CPSU-0010 | Y |
| Slide Rail | 9571CSLIDER-0010 | Y |
| Ear Rail | 9571CEAR-0010 | Y |

### Appendix 5: Content of Accessory Box (for ref.)

For GSe Pro 1004 series models

- One GUI CD pack, HW manual and operation manual inside

- One EonOne CD pack

- Two power cords

- One mini-USB to DB-9 cable

- 20 screws for HDD installation

- 16 screws for mounting enclosure to rack（M6 x4 and M5 x4 and #10-32 x4）

For GSe Pro 1008 series models

- One GUI CD pack, HW manual and operation manual inside

- One EonOne CD pack

- Two power cords

- One mini-USB to DB-9 cable

- 40 screws for HDD installation

- 16 screws for mounting enclosure to rack（M6 x4 and M5 x4 and #10-32 x4）

| Models | GSe Pro 1000 series |
| --- | --- |
| CPU | Intel CPU Avoton C2538 |
| RAID ENGINE | CPU/SW RAID |
| Memory socket | DDR3 x 2 sockets |
| DIMMs | 4GB DIMM x 1 (default) |
|  | (MAX 32GB per CTRL) |
| Flash ROM | 16M x 2 |
| NVRAM | FRAM FM21L16 (2Mbit) |
| Flash Module | m.2 64G MLC Flash |
| On Board LAN (1G) | RJ45 w/ 2 LED x 4 (88E1543) |
| M.2 connector | Yes x 1 |
| RS232 port | min USB |
| USB 2.0 | x2 |
| USB 3.0 | x2 |
| LED indicator | - Controller status |
|  | - CBM status |
|  | - Cache Dirty Status |
|  | - Host busy |
|  | - LAN Link |
|  | - LAN Active |
|  | - Restore Def |
|  | - 4*CH0 Link / Speed status (iSCSI 1G) |
|  | - 4*CH1 Link / Speed status (iSCSI 1G) |
| Push button | Yes (HW reserve only) |
| LCD/ LED PNL | LED support only |
| Buzzer | Yes |
| Driver Interface | SATA only |
| Drive chip | (1) Marvell 9235*1 (for GSe Pro 1008) |
|  | (2) Integrated SATA 3G port |
| Drive channel allocation | Please check the Block Diagram for details |
| Connector to BP | GSe Pro 1004: (1 x 5*6 pin connector + 1 x 9*6 pin “4 wall” Airmax) GSe Pro 1008: (1 x 5*6 pin connector + 2 x 9*6 pin “4 wall” Airmax) |
| I2C interface | YES |
| PCBA | 3822GSP04E (GSe Pro 1004) 3822GSP08E (GSe Pro 1008) |

Architecture for system block diagram

For GSe Pro 1004 series

GSe Pro 1008 series

ME Drawing

- Front view

1U4

2U8

- Rear view

1U4

2U8

- System

CTRL