| PROJECT NAME： GSe Pro 3008 series | Rev.：1.2 |
| --- | --- |
| DESCRIPTION: (ref): GSe Pro 3008 series 2U8-bay RAID subsystem, Generic controller, SATA, Single PSU, Intel Broadwell-DE 4-Core CPU D-1517 2U8-bay RAID subsystem, Generic controller, SATA, Redundant PSU, Intel Broadwell-DE 4-Core CPU D-1517 |
| PRODUCT MANAGER：Glenn.Lee | DATE：2017/07/07 |
| MODEL NAME / NUMBER : GSe Pro 3008 serial models GSe Pro 3008SP + dual optional host boards (4 in 1, iSCSI 10G (RJ45) , iSCSI 10G SFP+, SAS 12G, iSCSI 1G, Infiniband 56G x 2, iSCSI 40G x 2 , FC16 x2, FC16G x4, SAS 12G JBOD Expansions ) GSe Pro 3008RP + dual optional host boards (4 in 1, iSCSI 10G (RJ45) , iSCSI 10G SFP+, SAS 12G, iSCSI 1G, Infiniband 56G x 2, iSCSI 40G x 2 , FC16 x2, FC16G x4, SAS 12G JBOD Expansions ) |
| APPROVED： FW PM HW TM FW TM ME TM SW TM |
| PROJECT ORIGINATOR | PM MANAGER |
| NOTIFY： |
| SALE | SOFTWARE | HARDWARE | MFG. MGR. | GEN.MGR. |  |  |
| Change History List |
| Rev | Update Reason | Updated Date | Updated By | Approved By |
| 1.0 | New Release | 2017/06/06 | Glenn.Lee |  |
| 1.1 | Update Single PSU models | 2017/07/07 | Glenn.Lee |  |
| 1.2 | Remove Single PSU model | 2017/10/23 | Glenn.Lee |  |

Section 1: Overall view for whole product

| Category | Functional Specification | Remark |
| --- | --- | --- |
| Innovation | First IFT cloud gateway product |  |
| EonStor serial models products definition | Per C0 spec., EonStor GS serial models are: GSe Pro 3008SP GSe Pro 3008RP EonStor FS C0 MKT document: \\server02\Marketing\Product Planning\C0\Unify storage\Cloud Gateway HDD Bundle policy: Any number of "Drive + Plastic Tray" HDD types and q’ty are defined by Planning Cloud Gateway Product feature: Please follow the latest GS product feature: Host Board Support types: Models Host board types and ports Qty per CTRL GSe Pro 3000 series Converged host board (4 in 1) X 2 iSCSI 10G (RJ45) x 2 X 2 iSCSI 10G SFP+ x 2 X 2 SAS 12G x 2 X 2 iSCSI 1G x 4 X 2 FC16G x 2 X 2 FC16G x 4 X 2 iSCSI 40G QSFP+ x 2 X 2 Infiniband 56G QSFP+ x 2 X 2 SAS 12G x 2 for JBOD Expansions X 1 GSe Pro 3000 series Performance requirement: Product Family GSe Pro 3008 CPU BDE D-1517 Drive side interface SATA 6G GSe File read (MB/s) 400 GSe File write (MB/s) 400 GSe Pro 3000 series JBOD Support Models and Max Drive Policy: RAID Model Name Support JBOD Models Max Drive Number GSe Pro 3008 JB 3012A JB 3060/3060L 428 HDD GSe Pro 3000 series JBOD Support Configurations and Max Drive Policy: RAID Form-factor Recommended JBOD Configuration Total Number of Disks 2U8 RAID 3U12 x1 + JBOD 3U12 x 14 176 RAID 3U12 x1 + JBOD 4U60 x 7 428 GSe Pro 3000 Host board configurations list Host Board 1 Host Board 2 Converged host board (4 in 1) None iSCSI 10G (RJ45) x 2 None iSCSI 10G SFP+ x 2 None SAS 12G x 2 None iSCSI 1G x 4 None FC16G x 2 None FC16G x 4 None iSCSI 40G QSFP+ x 2 None Infiniband 56G QSFP+ x 2 None Converged host board (4 in 1) Converged host board (4 in 1) iSCSI 10G (RJ45) x 2 iSCSI 10G (RJ45) x 2 iSCSI 10G SFP+ x 2 iSCSI 10G SFP+ x 2 SAS 12G x 2 SAS 12G x 2 iSCSI 1G x 4 iSCSI 1G x 4 FC16G x 2 FC16G x 2 FC16G x 4 FC16G x 4 iSCSI 40G QSFP+ x 2 iSCSI 40G QSFP+ x 2 Infiniband 56G QSFP+ x 2 Infiniband 56G QSFP+ x 2 iSCSI 10G (RJ45) x 2 iSCSI 1G x 4 iSCSI 10G SFP+ x 2 FC16G x 2 iSCSI 10G SFP+ x 2 FC16G x 4 iSCSI 10G SFP+ x 2 Converged host board (4 in 1) iSCSI 1G x 4 FC16G x 2 iSCSI 1G x 4 Converged host board (4 in 1) FC16G x 4 iSCSI 10G SFP+ x 2 FC16G x 4 Converged host board (4 in 1) Converged host board (4 in 1) SAS 12G (for JBOD expansion) iSCSI 10G (RJ45) x 2 SAS 12G (for JBOD expansion) iSCSI 10G SFP+ x 2 SAS 12G (for JBOD expansion) SAS 12G x 2 SAS 12G (for JBOD expansion) iSCSI 1G x 4 SAS 12G (for JBOD expansion) FC16G x 2 SAS 12G (for JBOD expansion) FC16G x 4 SAS 12G (for JBOD expansion) iSCSI 40G QSFP+ x 2 SAS 12G (for JBOD expansion) Infiniband 56G QSFP+ x 2 SAS 12G (for JBOD expansion) |  |
| DIMM Configuration Requirements | Default configuration: 4GBx1 Support DDR4 up to 64G (32Gx2) Optional configurations: 8GB (4GBx 2), 16G (8G x2), 32G (16Gx2), 64G (32Gx2) |  |
| Push button requirement | For Reset CTRL to Restore default Status |  |
| LCD and LED Requirements | Only support LED PNL; LED follows ES_LED_FP_v1.22 or later version |  |
| HDD Support requirements | Support mixing SATA 3G/6G drives on AVL Support SATA-SSD (SSD: follow HDD AVL plan) |  |
| Form-factor requirements | Follow Enhance 3US and 2US ME design. |  |
| RoHS requirement | RoHS complaint is a MUST from development stage |  |
| PSU Requirements | For 2U12/3U16 platform: Delta-250W RAID Form-factor Enclosure Name Controller PSU Vendor 2U8 2US Generic 250 Watt Delta |  |
| Patent Concern | N.A. |  |
| MTBF | Controller: 500,000 hours Subsystem: 25,000 hours Power supplies: 250,000 hours Fans: 500,000 hours |  |
| EMC / Safety | Certification product names: should follow IFT business method of CTO EMC: BSMI, FCC / CE Class B (Class A is Acceptable). Safety: UL / cUL, CB, and ROSTEST (Russia Certificate) |  |
| Env. | Thermal: System working temperature should follow specs. Normal Operating: The temperature should be below 40C. Abnormal Operating (FANx1 or PSUx1 Failure): The temperature should remain below 40C Due to CPU spec, it cannot operate below 5C. Please test the system above 5C or equal to 5C to meet the CPU spec. Thermal concern Super Cap the Spec of Super cap is -25C~60C, Therefore it is recommend that w/o Super cap installed the room temperature cannot over 40C and W super cap installed the room temperature cannot over 40C. |  |
| Interoperability Req. | Refer to TD-4-06 Interoperability Test item of later version for SxF |  |

Section 2: User interface and customer related information

| Category | Functional Specification | Remark |
| --- | --- | --- |
| Connectors of rear-side of CTRL | For Single CTRL 1* mini USB connectors provide COM1 connectivity to HST. 1* RJ-45 connectors (1 in 1) provide 1GB Management function – on Main board 4* RJ-45 connectors (1 in 1) provide 1GB Fast Ethernet LAN connectivity – on Main board 1* USB 3.0 connector – on Main board |  |
| CTRL Drawing |  |  |
| LED indicator on CTRL | Please refer to ES_LED_FP_v1.22 or later version for detailed LED definitions Ctrl 1 LED in green/Amber, for Controller Status Ctrl 2 LED in amber, for Cache Dirty status Steady on 1. Cache Memory is dirty or 2. Flushing data from FBM to drive (when power back) Blink Writing cached data from cache memory to FBM* during power outage. Once writing is done, all LEDs are turned off. Off No data is in cache memory Note : FBM : Flash Backup Module Ctrl 3 LED in green, Fast Blink for Host Busy Restore Default Button: LED in GREEN, the default of NVRAM is restored Management Port *1 (1 in 1 connector): Speed LED on RJ-45 in green for 1G and blank for 10/100, Active LED Blink for LAN is active iSCSI 1G *4 ports (1 in 1 connector): Speed LED on 4x RJ-45 in green for 1G and blank for 10/100, Active LED Blink for LAN is active |  |
| Connectors of rear-side of Host Boards of a single CTRL | For iSCSI 1G 4* iSCSI 1G cages provide 1G connectivity to HST For iSCSI 10G (RJ45) 2* iSCSI 10G cages provide 10G/1G/100Mconnectivity to HST For iSCSI 10G (SFP+) 2* iSCSI 10G cages provide 10G connectivity to HST– (2 on each Host board) For SAS 12G (same for SAS 12G for JBOD Expansions) 2* SAS 12G cages provide 12/6/3G connectivity to HST– (2 on each Host board) For FCoE (4 in 1) 4* SFP+ cages provide FC 8G x 4 or FC 16G x 2 or iSCSI 10G SFP+ x 4 connectivity to HST– (4 on each Host board) For FC 16G x 2 2* FC 16G cages provide 16/8/4G connectivity to HST– (2 on each Host board) InfiniBand 56G (FDR) x2 2* InfiniBand 56G connectivity to HST– (2 on each Host board) For FC16G x4 4* SFP+ cages provide FC16G x 4 or FC 8G x 2 or FC4G x 4 connectivity to HST– (4 on each Host board) Ethernet 40G Host Board x2 2* 40G connectivity to HST– (2 on each Host board) |  |
| LED indicator on Optional Host Boards | iSCSI 1G x4 ports Host Board LED 8 x GbE LEDs (two on each GbE port) to indicate the speed/ link status For Speed LED: CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 LED on 1G 1G 1G 1G LED off 10/100Mbps 10/100Mbps 10/100Mbps 10/100Mbps For Link LED: CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 Steady on Link Link Link Link Blink Active Active Active Active Off No link No link No link No link ------------------------------------------------------------------------------------------------------------------------ iSCSI 10G (RJ45) x2 ports Host Board LED 4 x GbE LEDs (two on each GbE port) to indicate the speed/ link status For Speed LED: CH4/CH8 CH5/CH9 Green 10G 10G Amber 1G 1G LED off 100Mbps 100Mbps For link status LED: CH4/CH8 CH5/CH9 Steady on Link Link Blink Active Active Off No link No link ----------------------------------------------------------------------------------------------------------------------------- iSCSI 10G (SFP+) Host Board LED 1* CH0 LED in green, for CH0 link status Steady on Link Blink Active Off No link 1* CH1 LED in green, Steady On for CH1 link: spec is same as CH0 LED. ---------------------------------------------------------------------------------------------------------------------------- SAS 12G x2 ports Host Board LED (Same for SAS 12G host board support JBOD expansions) 2* LEDs (one for each host port), to indicate link status For Link status LED: CH4/CH8 CH5/CH9 Steady on Link Link Blink Active Active Off No link No link ---------------------------------------------------------------------------------------------------------------------------- 4 in 1 Host x4ports Board LED 8* LEDs (2 for each host port), to indicate link / speed status 2* Mode LEDs, to indicate mode status For Mode LED: 16G/8G - Green 16G Fiber mode (only 2 ports can support this mode) 16G/8G - Amber 8G Fiber mode 10G - Green 10G Ethernet mode For Link status LED: CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 Green Link Link Link Link Off No link No link No link No link For Speed LED (16G Fiber mode): CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 Green 16G 16G Amber 8G 8G Off 4G or no link 4G or no link For Speed LED (8G Fiber mode): CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 Green 8G 8G 8G 8G Amber 4G 4G 4G 4G Off 2G or no link 2G or no link 2G or no link 2G or no link For Speed LED (10G Ethernet mode): CH4/CH8 CH5/CH9 CH6/CH10 CH7/CH11 Green 10G 10G 10G 10G Amber Off No link No link No link No link -------------------------------------------------------------------------------------------------------------------------------- FC 16G x 2 Host Board LED 2* CH0/1 LEDs, to indicate CH0 link / speed status Link status LED: LED in Green for Link, and off for unlink Speed status LED: Green 16G Amber 8G LED off 4G 1* CH0 LED in green, for CH0 link status Steady on Link Blink Active Off No link --------------------------------------------------------------------------------------------------------------------------------- FC16G x 4 Host Board LED Each channel has three LED to indicate different speed as below showed. For 16G Speed LED: CH0 CH1 CH2 CH3 Green on Linked Green Blinking Data Transfer LED off No connect For 8G Speed LED: CH0 CH1 CH2 CH3 Green on Linked Green Blinking Data Transfer LED off No connect For 4G Speed LED: CH0 CH1 CH2 CH3 Amber on Linked Amber Blinking Data Transfer LED off No connect ------------------------------------------------------------------------------------------------------------------------------------------------ Ethernet 40G Host Board LED 2* CH0/1 LEDs, to indicate CH0 link / speed status Link status LED: LED in Green for Link, and off for unlink Speed status LED: Green Link Amber Active LED off Not connected |  |

Section 3：CTRL PCBA and Host Board PCBA requirement

| Category | Functional Specification | Remark |
| --- | --- | --- |
| 2U8: RAID engine G Models CTRL PCBA (3841GSP08E) | For GSe Pro 3008 Models CTRL : For 2U8 serial RAID engines CTRL use the same PCBA (PCBA named as 3841GSP08E) |  |
| RAID engine Host Boards: | For RAID engine Host Boards : iSCSI 1G 4 ports host boards 9483CE1HIO4 iSCSI 10G (SFP+) 2 ports host boards 9483CE1HIO2 iSCSI 10G (RJ45) 2 ports host boards 9483CE2HIO2 SAS 12G 2 ports host boards 9483CS2HIO2 4 in 1, 4 ports host boards 9483CC1HIO4 FC16G 2 ports host boards 9483CF9HIO2 FC16G 4 ports host boards 9483CF9HIO4 Infiniband 2 ports host boards 9483CE3HIO2 iSCSI 40G 2 ports host boards 9576CE4HIO2 SAS 12G 2 ports for JBOD Expansions host boards 9483CSJHIO2 |  |
| DRV backplanes | Different products use different Base-units w/ DRV BP PCBAs. And naming are listed as below: F/F G/R Base-unit DRV BP PCB DRV BP PCBA Models 2U8 G ESS12G2B2Dx-0035 9583ADP08G 9583ADP08G GSe Pro 3008 Note 1. D means EonStor DS, x=0 means no bundle HDD and x=P means half qty of bundle HDD (8 for 3U, and 6 for 2U) Please refer to ESS16F-X1840_FTS_V1.0 or later version for detail spec Please refer to \\Server02\pm\PCC infor system\A667_models_naming for Enclosure/PCBA naming |  |
| Other small boards: | Power board: 9583PWR2U 2U height, redundant PSU design. Adaptor board: 9583ADP To access Power board and Backplane. |  |
| Cache Backup Module for Caching Data | R CTRLs are having Cache Backup Module for default. G CTRLs are option. |  |
| FW feature spec | Use FW v3.91 or later version (follow EonStor G6) |  |
| SW feature spec | Use SW v2.3.x or later version (follow EonStor G6) |  |

Appendix 1: CTRL Key parts and general information of each model

| Controller | DS RAID CTRL |
| --- | --- |
| 3841GSP08E | GSe Pro 3008 |
| Host Boards | DS RAID Host Board |
| iSCSI 1G 4 ports host boards 9483CE1HIO4 | GSe Pro 3008 |
| iSCSI 10G (SFP+) 2 ports host boards 9483CE1HIO2 |  |
| iSCSI 10G (RJ45) 2 ports host boards 9483CE2HIO2 |  |
| SAS 12G 2 ports host boards 9483CS2HIO2 |  |
| 4 in 1, 4 ports host boards 9483CC1HIO4 |  |
| FC16G 2 ports host boards 9483CF9HIO2 |  |
| FC16G 4 ports host boards 9483CF9HIO4 |  |
| Infiniband 2 ports host boards 9483CE3HIO2 |  |
| iSCSI 40G 2 ports host boards 9576CE4HIO2 |  |
| SAS 12G 2 ports host boards 9483CSJHIO2 |  |
| Memory module per CTRL |  |
| DDR4 RDIMM 4GB | Default, 4GB*1 |
| DDR4 RDIMM 8GB | Optional, 4GB*2 |
| DDR4 RDIMM 16GB | Optional, 8GB*2 |
| DDR4 RDIMM 32GB | Optional, 16GB*2 |
| DDR4 RDIMM 64GB | Optional maximum, 32GB*2 |

Appendix 2: Spare parts and Accessories

| CTRL FRU P/N | GSe Pro 3008 |
| --- | --- |
| 3841GSP08E | V |

| GSe Pro 3000 Series |
| --- |
| BP FRU P/N | GSe Pro 3008 |
| 9583ADP08G | V |
| Host Board FRU P/N | GSe Pro 3008 |
| iSCSI 10G SFP+ (RES10G1HIO2-0010) | Y |
| iSCSI 10G RJ45 (RES10G1HIO2-0010) | Y |
| SAS12G (RSS12G1HIO2-0010) | Y |
| 4 in 1 (RFE16G1HIO4-0010) | Y |
| iSCSI 1G RJ45 (RER01G1HIO4-0010) | Y |
| FC16G x 2 (RFC16G1HIO2-0010) | Y |
| FC16G x 4 (RFC16G1HIO4-0010) | Y |
| iSCSI 40G x 2 (RER40G1HIO2-0010) | Y |
| SAS12G (RSS12J1HIO2-0010) | Y |
| Level-1 | Level-2 | FRU P/N | GSe Pro 3008 |
| Cables | FC | 9270CFCCab04-0010 | Y |
|  |  | 9270CFCCab05-0010 | Y |
|  |  | 9270CFCCab06-0010 | Y |
|  | Mini SAS 4X(SFF-8088) to Mini SAS 4X(SFF-8088) | 9270CmSASCab1-0030 (0.5M) | Y |
|  |  | 9270CmSASCab2-0030 (1.2M) | Y |
|  |  | 9270CmSASCab6-0030 (1.7M) | Y |
|  |  | 9270CmSASCab7-0030 (2.6M) | Y |
|  | SAS 12G Cables | 9370CmSASCab1-0030 (0.5M) | Y |
|  |  | 9370CmSASCab2-0030 (1.2M) | Y |
|  |  | 9370CmSASCab3-0030 (2.6M) | Y |
|  | Mini USB Cable | 9370ASCAB-0010 | Y |
| SFP module | 8G | 9370CSFP8G-0010 | Y |
|  | 10G | 9370CSFP10G-0010 | Y |
|  | 16G | 9370CSFP16G-0010 | Y |

### 2. Enclosure FRU

| Level-1 | FRU P/N | GSe Pro 3008 |
| --- | --- | --- |
| PSU | 9583CPSU-0010 | Y |
| Slide Rail | 9571CSLIDER-0010 | Y |
| Ear Rail | 9571CEAR-0010 | Y |

### Appendix 5: Content of Accessory Box (for ref.)

For GSe Pro 3008 series models

- One GUI CD pack, HW manual and operation manual inside

- One EonOne CD pack

- Two power cords

- One mini-USB to DB-9 cable

- 40 screws for HDD installation

- 16 screws for mounting enclosure to rack（M6 x4 and M5 x4 and #10-32 x4）

| Models | GSe Pro 3008 series + Optional Host Boards |
| --- | --- |
| CPU | Intel CPU Broadwell-DE D-1517 (3841GSP08E) |
| RAID ENGINE | CPU/SW RAID |
| Memory socket | DDR4 x 2 sockets |
| DIMMs | 4GB RDIMM x 1 (default) |
|  | (MAX 64GB per CTRL) |
| Flash ROM | 16M x 2 |
| NVRAM | FRAM FM21L16 (2Mbit) |
| Flash Backup Module | m.2 64G MLC Flash |
| Configuration LAN chip | Broadwell-DE + Intel i218 |
| Configuration LAN port | RJ45 w/ 2 LED x 1 (phy) |
| On Board LAN (1G) | RJ45 w/ 2 LED x 4 (i210) |
| M.2 connector | Yes x 1 |
| RS232 port | min USB |
| USB 3.0 | x1 |
| LED indicator | - Controller status |
|  | - CBM status |
|  | - Cache Dirty Status |
|  | - Host busy |
|  | - LAN Link |
|  | - LAN Active |
|  | - Restore Def |
|  | - 4*CH0 Link / Speed status (iSCSI 1G) |
|  | - 4*CH1 Link / Speed status (iSCSI 1G) |
| Push button | Yes (HW reserve only) |
| LCD/ LED PNL | LED support only |
| Buzzer | Yes |
| Driver Interface | SATA only |
| Drive chip | (1) Marvell 9235*1 |
|  | (2) Integrated SATA 6G port |
| Drive channel allocation | Please check the Block Diagram for details |
| Connector to BP | (1 x 5*6 pin connector + 2 x 9*6 pin “4 wall” Airmax) |
| I2C interface | YES |
| PCBA | 3841GSP08E + Optional Host Boards |

Architecture for system block diagram

For GSe Pro 3008 series

ME Drawing

- Front view

- Rear view

- System

- CTRL